## Slide 1
Project title
8x8 LED Matrix Scrolling Display with Arduino Control
Presented By:
Yogesh Kumar Chauhan 510617058
Nishant Bansal 510617062
Hariom Gupta 510617063
Ritik Raj 510617064
Kapil Agarwal 510617067
Jitin Chandolia 510617078

## Slide 2: INTRODUCTION
As written in the title this project contains a matrix of 64 LEDs to which we are giving inputs according to our pattern of data to show.
We have used a shift register and Arduino to give proper inputs to the matrix.
ThIs matrix can be used at many places like:
‘For conveying some message to people around it’.
‘For showing routes and destinations on buses’.

## Slide 3: Components used :
LED Lights
Arduino UNO
Shift Registor (SN74HC595N IC)
Resistors
Multimeter
Jumper Wires
Soldering Iron

## Slide 4
8x8 LED MATRIX
Construction
How to light up any particular LED in matrix ?
Need of resistance.
Where the problem arise?
Scaning.

## Slide 5
SIPO Shift Register IC(SN74HC595N)
Reduces the requirement of pins needed to connect LEDs to the microcontroller.
It contains two registers – ‘Shift Register’ and ‘Storage Register’ embedded in it.
Pin diagram of IC.
Working of the IC if input given to it is ‘11111111’ serially.
Timing diagram of SIPO Shift Register.

## Slide 6
Multiplexing technique
What is multiplexing technique?
Why do we use it?

## Slide 7: Arduino UNO(UNO R3)

## Slide 8: Circuit Diagram

## Slide 9: Sample Arduino Code (For static characters):
byte character[3][8]={{B00001110,//Character to be written
B00000100,
B00000100,
B00000100,
B00000100,
B01000100,
B00100100,
B00011100},
{B10000001,//Character to be written
B01000010,
B00100100,
B00011000,
B00001000,
B00001000,
B00001000,
B00001000},
{B01111110,
B00000010,
B00000100,
B00001000,
B00010000,
B00100000,
B01000000,
B01111110}};

## Slide 10
byte column_pin[8]={ 6, 7, 8, 9, 10, 11, 12, 13};
#define SER_PIN 3
#define SCK_PIN 5
#define RCK_PIN 4}
void setup()
{
// Turn everything to low
for(int i=0; i<8; i++) {
pinMode(column_pin[i],OUTPUT);
}
pinMode(SER_PIN, OUTPUT);
pinMode(SCK_PIN, OUTPUT);
pinMode(RCK_PIN, OUTPUT);
Serial.begin(9600);
}

## Slide 11
void loop()
{
// iterate each row
int rowbits = 0x80;
static int g=0;
for(int row=0; row<8; row++)
{
for(int k=0; k<8; k++)
digitalWrite(column_pin[k],HIGH); // Cleanup cols
writerow(rowbits); // prepare to write the row
for(int col=0; col<8; col++)
{
digitalWrite(column_pin[7-col], character[(g/100)%3][row] & 1 << col ? LOW : HIGH);
}
delay(1);
writerow(0);
rowbits >>= 1;
}
g=g+1;
}

## Slide 12
void writerow(byte data)
{
digitalWrite(RCK_PIN, LOW);
shiftOut(SER_PIN, SCK_PIN, LSBFIRST, data);
digitalWrite(RCK_PIN, HIGH);
}

## Slide 13: Sample Arduino Code (Scrolling characters):
byte characters[5][8] = {
// H
{B10000001,
B10000001,
B10000001,
B11111111,
B10000001,
B10000001,
B10000001,
B10000001},
// E
{B11111111,
B10000000,
B10000000,
B11111110,
B10000000,
B10000000,
B10000000,
B11111111},

## Slide 14
// L
{B10000000,
B10000000,
B10000000,
B10000000,
B10000000,
B10000000,
B10000000,
B11111111},
// L (repeated)
{B10000000,
B10000000,
B10000000,
B10000000,
B10000000,
B10000000,
B10000000,
B11111111},

## Slide 15
// O
{B01111110,
B10000001,
B10000001,
B10000001,
B10000001,
B10000001,
B10000001,
B01111110}};
byte column_pin[8] = { 6, 7, 8, 9, 10, 11, 12, 13 };
#define SER_PIN 3
#define SCK_PIN 5
#define RCK_PIN 4

## Slide 16
void setup()
{ // Turn everything to low
for(int i = 0; i < 8; i++) {
pinMode(column_pin[i], OUTPUT);
}
pinMode(SER_PIN, OUTPUT);
pinMode(SCK_PIN, OUTPUT);
pinMode(RCK_PIN, OUTPUT);
Serial.begin(9600);
}
void loop() {
static int position = 0; // Position of the scrolling text
for(int i = 0; i < 8; i++) {
displayCharacter(position, i); delay(2); // Adjust speed of scrolling
}
position++; // Move to the next column
if (position >= 8 * 5) { // Reset position after complete scroll
position = 0;
}
}

## Slide 17
void displayCharacter(int position, int row) {
  int charIndex = position / 8; // Determine which character to display
  int columnShift = position % 8; // Determine the column shift
  for(int col = 0; col < 8; col++) {
  // Write the shifted character to the matrix
  int characterColumn = (characters[charIndex][row] >> columnShift) & 0x01; digitalWrite(column_pin[7 - col], characterColumn ? LOW : HIGH);
}
writerow(0x80 >> row); // Write the row data
}
void writerow(byte data) {
  digitalWrite(RCK_PIN, LOW);
  shiftOut(SER_PIN, SCK_PIN, LSBFIRST, data);
  digitalWrite(RCK_PIN, HIGH);
}

## Slide 18: Application:
For Displaying Information
In Public Transportation Vehicles
In Large Displays
In Traffic Signalling

## Slide 19
Advantages:
Used in advertisement
Difficult to damage with external shock
Relatively long useful life
Small and easily populated onto PCBs
Good efficiency
Disadvantages:
Colour uniformity
Limitation on character size
Output has not high resolution
Pins can bend easily
Print quality

## Slide 20: THANK YOU.